## Slide 1: SMART WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION SYSTEM WITH SENSORS FUSION
Sreelakshmi Hari
Class no:59 s7 Btech CSE
12 SEPTEMBER,2018

## Slide 2: CONTENTS
INTRODUCTION
VISION METHOD
SYSTEM DESIGN
OVERVIEW
METHOD
SIGN CLASSIFIER
RESULT
CONCLUSION
REFERENCES
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 3: INTRODUCTION
Sign language plays a vital role in deaf and mute people.
Languages have been recognized using two major techniques.
                Non vision approach
                Vision approach
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 4: VISION METHOD
System that uses a camera
This method divided into:
        Direct approach
        Indirect approach
Affected by image filtering ,color segmentation and background cancellation.
Non-vision approach utilize sensors.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Notes: Direct based on rgb color spaces of the skin color
Indirect using data glove

## Slide 5: INTRODUCTION(Contd..)
Gestures are identified using
          5 flex sensors
          2 pressure sensors
          IMU sensor
          gyroscope sensor
Gestures are recognized using SVM model.
Received through wireless Bluetooth transmission
Text to speech converted into audible form
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 6: SYSTEM DESIGN
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314694

## Slide 7: HARDWARE DESIGN AND SYSTEM FLOW
Flex sensors :- omnidirectional and bidirectional sensors.
Bidirectional type is used with each flex sensor is of 10kΩ resistor
Proposed system divided into 3 modules:
                Sensor module
                Processing module
                Application module
Sensor and processing modules : wearable device.
Application module : Android-based mobile device.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 8: OVERVIEW DESIGN
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314694

## Slide 9: HARDWARE DESIGN AND SYSTEM FLOW(Contd.)
Flex sensors and IMU data are collected using an ArduinoPro Mini328.
Data extracted from sensor data and serve to SVM
28 gesture patterns - 26 alphabets ,a neutral state and an invalid sign.
Detected sign is transmitted using Bluetooth module.
Recieved text will display on the screen.
Then text to speech converted into audible form.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 10: METHODS
Preprocessing
Feature Extraction
Sign classifier
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 11: PREPROCESSING
Flexion values varies among hands
Resistance of flex sensors in smaller hand will have less variation
Sensor values are normalized on computed mean and standard deviation
𝑓𝑠𝑖̂=(𝑓𝑠𝑖−𝑓𝑠̅) / 𝜎𝑓𝑠
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 12: PREPROCESSING(Contd..)
The hand movement derived from the IMU in three orientation:
                Pitch
                Roll
                Yaw
Sign gestures are:
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314695

## Slide 13: FEATURE EXTRACTION
The flexion degree is split into three regions
        first region -“no bend” or “slight bend,”
        second region is considered as a “partial bend”
        Last region is a “complete bend”
These regions are abbreviated in order as:
        OR
        PR
        CR
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 14: FEATURE EXTRACTION(Contd..)
Signs exhibit the same regions :
“U” and “V,” “K” and “P,” and “I” and “J,” as well as “G,” “L,” “Q,” and “Z.”
Addition of pressure sensors :two Flexi force pressure sensors used
Surface is pressed ,resistance of a Flexi force pressure sensor is reduced.
The pressure sensors are connected to the digital inputs in processing module
            “0” if pressure sensor surface is not pressed
            “1” if the pressure is sensed on the surface of the sensor
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 15: FEATURE EXTRACTION(Contd..)
Inclusion of the pressure sensors - solve issues of the letters “U” and “V”
SDs of letter “I” are approximately 0.0369 (pitch), 0.0151 (roll), 0.0375 (yaw)
SDs of letter “J” are 1.3968 (pitch), 0.5603 (roll), and 1.1548 (yaw)
The calculation of each orientation is depending on axis.
𝑎𝑔𝑙𝑖=0.98×(𝑎𝑔𝑙𝑖−1+𝑔𝑦𝑟𝑖/𝑔𝑦𝑟𝐻𝑍)+𝑎𝑔𝑙𝑐𝑖×0.02,
𝑎𝑔𝑙𝑐𝑖= arctan(𝐴𝑢,𝐴𝑣)×180/𝜋
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 16: FEATURE EXTRACTION(Cont.)
𝐴𝑢 and 𝐴𝑣 are denoted as the y-axis and z-axis of accelerometer readings.
Wearable device with fusion of pressure sensor
Courtesy:https://ieeexplore.ieee.org/document/8314694
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 17: SVM
SVM are a set of methods for binary supervised learning
Applicable to both classification and regression problems
SVM classifiers creates maximum-margin hyperplane
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 18: LINEAR CLASSIFIERS
f
x
y
denotes +1
denotes -1
f( x,w ,b ) = sign(w. x - b)
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
w: weight vector
x: data vector
b: scale value
Courtesy:https://ieeexplore.ieee.org/document/8314664

## Slide 19: MAXIMUM MARGIN
d+
d-
The distance between H and H1
w•x+b|/||w||=1/||w||
The distance between H1 and H2 : 2/||w||
Maximize the margin, we need to minimize ||w||.
No datapoints between H1 and H2:
xi•w+b  +1 when yi =+1
xi•w+b  -1 when yi =-1
H1
H2
H
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314664

## Slide 20: SIGN CLASSIFIER
The SVM is trained using the “leave one subject out” (LOO) method.
SVM is trained using n – 1 subject datasets, n is the total number of subjects.
The accuracy of each trained model is computed as
𝐴𝐶=𝑇𝑃+𝑇𝑁 / 𝑇𝑃+𝑇𝑁+𝐹𝑃+𝐹𝑁
𝑇𝑃, 𝑇𝑁 - are true positive, true negative.
𝐹𝑃, and 𝐹𝑁 - false positive and false negative respectively.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 21: SIGN CLASSIFIER(Cont.)
LOO method is best to utilize for model training
It is suitable method to estimate the risk when learning a model.
SUBJECT SAMPLE SIZE((TP + TN) / Total) AC (%)
1st version 425,736 / 648,000 65.7
2nd version 636,336 / 648,000 98.2
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 22: RESULT
when two pressure sensors data is used
        Mean AC of ”U” of 57.25% to 97.52%
        Mean AC of “R” increased from 57.78% to 97.28%
        Mean AC of “V” increased from 57.22% to 97.49%
.
Inclusion of pressure sensor surface showed differences for “U” and “V.”
.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 23: RESULT(Cont.)
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314664

## Slide 24: SIGN INTERPRETATION
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION
Courtesy:https://ieeexplore.ieee.org/document/8314694

## Slide 25: CONCLUSION
Android mobile application was developed for text-to-speech service.
Comfort
Flexible
Eliminating the necessity of custom-made devices
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 26: REFERENCES
J. Wang and T. Zhang, “An ARM-based embedded gesture recognition system using a data glove,” presented at the 26th Chinese Control and Decision Conf., Changsha, China, May 31 - June2, 2014.
A. Z. Shaker, M. F. Miskon, M. H. Jamaluddin, F. A. Ibrahim, M. F. Asyraf and M. B. Bahar, “A new data glove approach for Malaysian sign language detection,” Procedia Comput. Sci., vol. 76, no. 1, pp. 60-67, Dec. 2015.
N. Sri ram and M. Nithiyanandham, “A hand gesture recognition based communication system for silent speakers,” presented at the Int. Conf. Human Comput . Interact., Chennai, India, Aug. 23-24, 2013.
J. Galka , M. Masior , M. Zaborski, K. Barczewska, “Inertial motion sensing glove for sign language gesture acquisition and recognition,” IEEE Sensors J., vol. 16, no. 16, pp. 6310-6316, Aug. 2016.
X. Cai, T. Guo, X. Wu and H. Sun, “Gesture recognition method based on wireless data glove with sensors,” Sensor Letters, vol. 13, no. 2, pp. 134-137, Feb. 2015.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 27: REFERENCES(Contd..)
6. K. Liu, C. Chen, R. Jafari and N. Kehtarnavaz, “Fusion of inertial and depth sensor data for robust hand gesture recognition,” IEEE Sensors J., vol. 14, no. 6, pp. 1898-1903, Jun. 2014.
7. K. W. Kim, M. S. Lee, B. R. Soon, M. H. Ryu and J. N. Kim, “Recognition of sign language with an inertial sensor-based data glove,” Technol. Health Care, vol. 24, no. 1, pp. 223-230, 2016.
8. L. Sousa, J. M. F. Rodrigues, J. Monteiro, P. J. S. Cardoso and R. Lam, “GyGSLA: a portable glove system for learning sign language alphabet,” presented at Int. Conf. Universal Access in Human-Comput. Interact., Toronto, ON, Canada, Jul. 17-22, 2016.
9. N. Caporusso, L. Biasi, G. Cinquepalmi, G. F. Trotta and A. Brunetti, “A wearable device supporting multiple touch- and gesture-based languages for the deaf-blind,” presented at Int. Conf. Appl. Human Factors and Ergonomics, LA, CA, USA, Jul. 17-21 2017.
10. Z. Yu, X. Chen, Q. Li, X. Zhang and P. Zhou, “A hand gesture recognition framework and wearable gesture-based interaction prototype for mobile devices,” IEEE Trans. Human-Mach. Syst., vol. 44, no. 2, pp. 293-299, Apr. 2014.
WEARABLE HAND DEVICE FOR SIGN LANGUAGE INTERPRETATION

## Slide 28
THANK YOU